Encryption in SD

Encryption, Decryption and Encoding are handled by the libsodium package https://doc.libsodium.org

Calling syntax:

encrypted_text = SDENCRYPT(Data, KeyToUse, Encoding)
   where:
Data	= string to encrypt
KeyToUse	= Encoded string which will decode to a crypto_secretbox_KEYBYTES bytes	sized key (currently defined as 32 bytes / 256 bits).
Encoding	= one of:
        SD_EncodeHX - The key and returned encrypted text are Hex Encoded	(passed key is	a 64 Character Hex encoded string which will be converted	to 32 bytes, encrypted text will be a Hex encoded character String 2X the	length of the passed string to encrypt).
        SD_Encode64 - The key and returned encrypted text are Base64 Encoded
(passed key is	a 44 Character Base64 encoded string which will be	converted to 32 bytes, encrypted text will be a Base64 encoded character	String ).

 decrypted_text = SDDECRYPT(Data, KeyToUse, Encoding)
   where:

       Data	= encrypted string
       KeyToUse	= Encoded string which will decode to a crypto_secretbox_KEYBYTES bytes	sized key (currently defined as 32 bytes / 256 bits).
        Encoding	= one of:
        SD_EncodeHX - The key and passed encrypted text are Hex Encoded (passed	key is a 64 Character Hex string which will be converted to 32 bytes,	encrypted text will be a Hex Character String 2X the length of the	returned decrypted text).
        SD_Encode64 - The key and passed encrypted text are Base64 Encoded

Why libsodium ?
From https://doc.libsodium.org/
Sodium is a modern, easy-to-use software library for encryption, decryption, signatures, password hashing, and more.
To use this extension you need to install libsodium-dev and libsodium23 (Ubuntu):
   apt install libsodium-dev libsodium23
Encryption, Decryption and encoding using libsodium package:
https://doc.libsodium.org/
This routine (and doc) is based on information found here:
https://doc.libsodium.org/secret-key_cryptography/secretbox
https://github.com/jedisct1/libsodium/blob/master/test/default/secretbox_easy2.c
https://doc.libsodium.org/password_hashing/default_phf
SD encrypts using crypto_secretbox_easy:
   int crypto_secretbox_easy(unsigned char *c, const unsigned char *m,
        unsigned long long mlen, const unsigned char *n,
        const unsigned char *k)
The crypto_secretbox_easy() function encrypts a message m whose length is mlen bytes, with a key k and a nonce n.
k should be crypto_secretbox_KEYBYTES bytes (currently defined as 32 bytes / 256 bits) and n should be crypto_secretbox_NONCEBYTES bytes.
c should be at least crypto_secretbox_MACBYTES + mlen bytes long.
This function writes the authentication tag, whose length is crypto_secretbox_MACBYTES bytes,
in c, immediately followed by the encrypted message, whose length is the same as the plaintext: mlen.
Functions returning an int return 0 on success and -1 to indicate an error.
   REM:
     A 128-bit (16 byte) key can be expressed as a hexadecimal string with 32 characters.
       It will require 24 characters in base64.
     A 256-bit (32 byte) key can be expressed as a hexadecimal string with 64 characters.
       It will require 44 characters in base64.
   Note we return the encryption output with the nonce appended to the end
   Rem to encode either base64 or hex before returning to SD!
SD decrypts using crypto_secretbox_open_easy:
   int crypto_secretbox_open_easy(unsigned char *m, const unsigned char *c,
        unsigned long long clen, const unsigned char *n,
        const unsigned char *k);
   c is a pointer to an authentication tag + encrypted message combination,
   as produced by crypto_secretbox_easy().
   clen is the length of this authentication tag + encrypted message combination.
   Put differently, clen is the number of bytes written by crypto_secretbox_easy(),
   which is crypto_secretbox_MACBYTES + the length of the message.
The nonce n and the key k have to match those used to encrypt and authenticate the message.
The function returns -1 if the verification fails, and 0 on success.
On success, the decrypted message is stored into m.
If the user wishes to use a password for encryption / decryption we need to generate a key for it.
The project recommends using crypto_pwhash to convert a password to a key, but to be reproducible the routine requires:
The salt to be know
Values for opslimit and memlimit
https://doc.libsodium.org/key_derivation and https://doc.libsodium.org/password_hashing/default_phf
To do this we will use function:
   int crypto_pwhash(unsigned char * const out,
        unsigned long long outlen,
        const char * const passwd,
        unsigned long long passwdlen,
        const unsigned char * const salt,
        unsigned long long opslimit,
        size_t memlimit, int alg);
The crypto_pwhash() function derives an outlen bytes long key from a password passwd whose length is passwdlen and a salt whose fixed length is crypto_pwhash_SALTBYTES bytes.
Passwdlen should be at least crypto_pwhash_PASSWD_MIN and crypto_pwhash_PASSWD_MAX.
outlen should be at least crypto_pwhash_BYTES_MIN = 16 (128 bits) and at most crypto_pwhash_BYTES_MAX.
The salt should be unpredictable. randombytes_buf() is the easiest way to fill the crypto_pwhash_SALTBYTES bytes of the salt.
Keep in mind that to produce the same key from the same password, the same algorithm,
the same salt, and the same values for opslimit and memlimit must be used.
SD provides two subroutines to support password to key creation:

!SD_GET_SALT(mysalt) - creates a base64 encoded salt and returns in mysalt.

!SD_KEY_FROM_PW(mypassphrase, mysalt, mykey) – creates a base64 encoded key returned in
        mykey. Where:
mypassphrase is a text password / phrase
mysalt – is a base64 encoded salt created via !SD_SALT()*

*This setup requires the user to save the salt used for key generation.

There is an example of usage found in BP/SD_ENCRYPT_EXT